## Slide 1: Multiple View Geometry for Robotics

## Slide 2: Multiple View Geometry for Robotics
Estimate 3D Motion of the Robot
Estimate the Geometry of the World (Depth of Scene and Shape)
Estimate the Movement of Independently Moving Objects
Motion Tracking
Navigation
Manipulation

## Slide 3: Scenarios
The two images can arise from
A stereo rig consisting of two cameras
  the two images are acquired simultaneously
or
A single moving camera (static scene)
  the two images are acquired sequentially
The two scenarios are geometrically equivalent

## Slide 4
Stereo head
Camera on a mobile vehicle

## Slide 5: Image Formation
Pinhole
Frontal pinhole

## Slide 6: Pinhole Camera Model
Image coordinates are nonlinear function of world coordinates
Relationship between coordinates in the camera frame and sensor plane
2-D coordinates Homogeneous coordinates

## Slide 7: Image Coordinates
CS482, Jana Kosecka
pixel coordinates
Relationship between coordinates in the sensor plane and image
metric coordinates
Linear transformation

## Slide 8: Calibration Matrix and Camera Model
Relationship between coordinates in the world frame and image
Intrinsic parameters
Pinhole camera Pixel coordinates
Adding transformation between camera coordinate systems and world coordinate system
Extrinsic Parameters

## Slide 9: Transformation between 2 views Camera parameters :
Intrinsic parameters: ( Calibration parameters)
  Principal point coordinates
  Focal length
  Pixel magnification factors
  Skew (non-rectangular pixels)
  Radial distortion
Extrinsic parameters
  Rotation and translation relative to world coordinate system

## Slide 10
Kosecka, CS 685
18
Homogeneous coordinates of a 3-D point
Homogeneous coordinates of its 2-D image
Image of a Point
Projection of a 3-D point to an image plane

## Slide 11
The epipolar geometry
C,C’,x,x’ and X are coplanar

## Slide 12
The epipolar geometry
All points on p project on l and l’

## Slide 13: Epipolar constraint (general case)
X
x
x’ = Rx+t
R
t
The vectors Rx, t, and x’ are coplanar
= (x,1)T
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 14: Epipolar constraint: Calibrated case
X
x
x’ = Rx+t
Essential Matrix
(Longuet-Higgins, 1981)
The vectors Rx, t, and x’ are coplanar

## Slide 16: Two View Geometry
When a camera changes position and orientation, the scene moves rigidly relative to the camera
3-D
Scene
u
u’
Rotation + translation

## Slide 17
3-D
Scene
Rotation + translation
u
u’
Objective:
find formulas that links corresponding points

## Slide 18: Two View Geometry (simple cases)
In two cases this results in homography:
  Camera rotates around its focal point
  The scene is planar
  Then:
  Point correspondence forms 1:1mapping
  depth cannot be recovered

## Slide 19: Camera Rotation
(R is 3x3 non-singular)

## Slide 20: Planar Scenes
Intuitively
  A sequence of two perspectivities
Algebraically
Need to show:
Scene
Camera 1
Camera 2

## Slide 21: Summary: Two Views Related by Homography
Two images are related by homography:
One to one mapping from p to p’
H contains 8 degrees of freedom
Given correspondences, each point determines 2 equations
4 points are required to recover H
Depth cannot be recovered

## Slide 22: Stereo
Assumes (two) cameras.
Known positions.
Recover depth.

## Slide 23: Depth from disparity
f
x
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth!
B1
B2

## Slide 24: Active stereo with structured light
Project “structured” light patterns onto the object
  Simplifies the correspondence problem
  Allows us to use only one camera
camera
projector
L. Zhang, B. Curless, and S. M. Seitz. Rapid Shape Acquisition Using Color Structured Light and Multi-pass Dynamic Programming. 3DPVT 2002

## Slide 25: Active stereo with structured light
L. Zhang, B. Curless, and S. M. Seitz. Rapid Shape Acquisition Using Color Structured Light and Multi-pass Dynamic Programming. 3DPVT 2002

## Slide 26: Active stereo with structured light
http://en.wikipedia.org/wiki/Structured-light_3D_scanner

## Slide 27: Kinect: Structured infrared light
http://bbzippo.wordpress.com/2010/11/28/kinect-in-infrared/

## Slide 28: Kinect 1
Kinect uses a speckle pattern of dots that are projected onto a scene by means of an IR projector, and detected by an IR camera.
Each IR dot in the speckle pattern has a unique surrounding area and therefore allows each dot to be easily identified when projected onto a scene. The processing performed in the Kinect in order to calculate depth is essentially a stereo vision computation.